## Slide 1: Items that interested me at APIC 2015
Barbara A. Smith
Thank you for the support to attend APIC 2015

## Slide 2: Evidence behind the new guidelines for reprocessing flexible endoscopes and Reprocessing endoscopes in ambulatory care settings
Ofstead, Wetzler, Eiland, Rocco

## Slide 3: Risk of transmission
Oft quoted statistics of 1 infection in 1.8 million by endoscope
Extrapolated from review articles and estimated # of procedures in US
Yet…
2010- Hennepin MC: incorrect info from manufacturer led to notification of 2600 pts
2009 FDA – 9 cases C. diff
2013- est. 6- 42 % attack rates for ERCP scopes (different locations)
LA: 2 deaths – 2015
Seattle – 11 deaths – 2014
Chicago – 2 deaths- 2014

## Slide 4: Results of inspections
Date | State | Reason for visit | Findings
2010 | CA | routine | Lack of tracking Expired HLD
2010 | MN | complaint | Blood on scope Incorrect connector
2011 | NJ | routine | Lack of competency demonstration Incorrectly performed leak test
2011 | NV | complaint | Dripping scopes
2011 | NJ | routine | Lack of PPE and hand washing

## Slide 5: 2 phase study of HLD

## Slide 6: Factors impacting risk
Procedural | Patient | Community | Facility
Entry point | Age | Prevalence of BBP | Outpatient vs. inpatient
Organ of interest | Comorbidities | Antimicrobial usage | Age of scopes
Reprocessing delays | Severity of illness |  | Quality of reprocessing
Mucus membranes disrupted | Immune compromised |  | Monitoring of reprocessing
 | Hx of antimicrobials |  | Response to breaches
 | Interventions during case |  | Use of electronic data

## Slide 7: Assessing your practice
DO the scopes or cabinets smell bad
Can you smell chemicals
How are the scopes stored
Are there stains in the cabinet
Does # of MEC strips coincide with # of cases
Are logs UTD:
  Cycle complete, Leak test, HLD temp and mec, filter changes, maintenance

## Slide 8: Improving practice
Perform audits
Cleanliness effectiveness checks
Inspect channels with bore scope
Periodic microbial cultures
Engage manufacturers

## Slide 9: More strategies
Read all instructions for use
  Which may differ from published guidelines
  Example of maximal storage time
Automate whenever possible
Make sure adequate room for reprocessing

## Slide 10: Using data for prevention: what’s on TAP in your hospital Target – Assess - Prevent
Gould/ Dudeck/ Soe

## Slide 11: TAP strategy
Target
TAP report in NHSN
Identify units with > HAIs
Assess
Assess for gaps
Prevent
Feedback to units
Links to implementation guides
Engage group
Measure practices
Assessment tools
Evaluate interventions

## Slide 12: How derived in NHSN
Annual survey
Rate tables
SIRS
Event level info (CLABS and Cauti)
www.cdc.gov/hai/prevention/tap.html
Designed to compare to HHS SIR targets
  CLABS - 0.5
  CAUTI – 0.75
  CDI- 0.7

## Slide 13: What do IPs want to know? A review of queries from IP talk and APIC.org
Landers/Gase

## Slide 14: Methods
Classified IP talk content
Classified apic.org searches
Compared the two results
Prioritize research topics

## Slide 15: What’s there- IP talk
IP talk | Material
15,556 members 34,000 discussions 1,300 library items | Presentations- one EVS example 1652 downloads Video- 428 downloads Document - 1727 downloads

## Slide 16: What’s there – APIC.org
37,728 visitors per month
404,407 page views
Page Rank of 6 – which is good

## Slide 17: Compared the topics on each
APIC competency mode:
  IP & C domain
  Technical
  Leadership /program management
  PI and implementation science
Infection – organism
Infection – type
Practice – hand hygiene
Practice - isolation

## Slide 18: What they found
APIC.org | IP talk
CAUTI Hand hygiene Construction MRSA Ebola ESBL CCLABSI Risk assessment C. Difficile Epi 101 Library APIC text ICRA Bioterrorism Emerging infections Certification Antibiotic stewardship Ebola patient care protocol | Risk assessment Bed bugs MRSA Ebola Library Construction CAUTI Hand hygiene Rounds IC plan Ultrasound gel Stethoscopes IP week SSI Steriples Fans Nails

## Slide 19: Top downloads
Novice Roadmap Infection preventionist
New member brochure
IP competency model
CAUTI implementation guide
Duodenoscopes and other endoscope FDA letter

## Slide 20: Findings
Congruence between both searches
Limitations
  What IPs want to know; Not need to know
  May not be representative of all IPs
  Seasonal variations not accounted for
  Identified future research possibilities
  Hand hygiene and CAUTI

## Slide 22: Infection Prevention and You materials
ABC's of Antibiotics Flyer for patient
What are healthcare-associated infections?
Who are infection preventionists
Infection Prevention and You Infographic Flyer for patients
Infection Prevention and You - Isolation Precautions

## Slide 23: Volunteer
Conference Committee
Communications Committee
Education Committee
Emergency Preparedness
Member Services
Nominating and Awards.
Practice Guidance
Professional Development e.
Public Policy
Research Committee
CBIC- Board members, test writers, reviewers